## Slide 1: OneFi: One-Shot Recognition for Unseen Gesture via COTS WiFi
Rui Xiao, Jianwei Liu, Jinsong Han, Kui Ren
SenSys 2021

## Slide 2: Human Gesture Recognition (HGR)
Virtual Reality
Smart Home Automation
Medical Control
WiFi-based solution:
  No need to wear sensors
  Less intrusive to user privacy
  And also ubiquitous
Privacy Leakage
Uncomfortable

## Slide 3: WiFi-based HGR
Works under supervised learning scheme: Three phases
  Predefine base gestures
  Training data collection
  Model training
Base gestures:
Question: What if now we want to recognize unseen gestures which are not included in base gestures?
Push Forward
Draw Zig-Zag
Clap

## Slide 4: Unseen gestures are important.
Collect unseen gesture samples
Retrain the whole model
Please perform ‘wave’ for 20 times.
Predefined base gestures cannot keep up with ever-evolving demands.
It’s crucial to allow the user to adapt the system to their own preference.
However, in existing systems, to recognize unseen gestures …
Data Collection Overhead
Training Overhead
Limited Scalability

## Slide 5: Problem Definition
When introducing unseen gestures, is it possible that:
User only needs to collect one signal sample for any unseen gestures.
Model can fast adapt to new data without retraining the whole model.
This problem falls into the category of few shot learning.
-- Learning with a few samples.
Assume that our system can recognize a few base gestures.

## Slide 6: Few shot learning
Few shot learning is easy for human.
Because human beings have a large amount of prior knowledge.
One shot is enough.
Why?

## Slide 7: Few shot learning: Basics
In few shot learning context
  Training set is also called support set
  Testing set is also called query set
Model
Support Set
(Few shot samples)
Training Phase
Testing Phase
Query Set
Recognition Result
Base Dataset
prior knowledge
Model
No overlap with support set

## Slide 8: Existing works: Meta-learning as few shot solution
A simple view of meta-learning: learning to learn
Train a “learner” model:
Train a “Meta-learner”:
Normal Learning
Meta Learning
I’ll teach how to learn faster
Task 1:
Task 2:

## Slide 9: Existing works: Meta-learning as few shot solution
MetaSense (Gong et al, SenSys’19)
  New user and new device.
RF-Net (Ding et al, SenSys’20)
  New environments.
MetaSense
RF-Net

## Slide 10: Challenge 1: Insufficient Prior Knowledge
The base dataset in WiFi HGR system is usually small.
Therefore, the prior knowledge is usually insufficient.
We use 20 gestures as base classes and apply meta-learning scheme, the result of one shot recognition for unseen gestures is unacceptable:

## Slide 11: Challenge 2: Complicated Training Process
Meta-learning multiplies the complexity of the regular training process.
Extract Prior Knowledge from Base Classes
Unseen Gesture Training
Training Overhead
Task 1:
Task 2:

## Slide 12: Our Solution -- OneFi
Overview:
Enrich the prior knowledge
A data augmentation method based on signal modeling
Base Dataset
Pre-processing
Data Augmentation
Support Set
Pre-processing
Extract Prior Knowledge
One-Shot Adaption
(Solve Challenge 1)

## Slide 13: Our Solution -- OneFi
Overview:
Enrich the prior knowledge
A data augmentation method based on signal modeling
Base Dataset
Pre-processing
Data Augmentation
Support Set
Pre-processing
Extract Prior Knowledge
One-Shot Adaption
A similarity-based one-shot learning framework
Alleviate Training Overhead
A self-attention-based backbone
(Solve Challenge 1)
(Solve Challenge 2)

## Slide 14: Our Solution -- OneFi
Overview:
A similarity-based one-shot learning framework
Enrich the prior knowledge
Alleviate Training Overhead
A self-attention-based backbone
A data augmentation method based on signal modeling
Base Dataset
Pre-processing
Data Augmentation
Support Set
Pre-processing
Extract Prior Knowledge
One-Shot Adaption

## Slide 15: Data Augmentation – Generate Virtual Gestures
Generates additional, synthetic data by signal modeling
The intuition here is that we could generate a ‘push left’ gesture by rotating a ‘push forward’ gesture.
Push Forward
Push Left
Doppler Spectrogram

## Slide 16: Data Augmentation – Generate Virtual Gestures
Question: How to rotate a gesture?
Signal modeling is required!
We compute the velocity distribution of the gesture, and apply rotation on the velocity domain.

## Slide 17: Data Augmentation – Generate Virtual Gestures
We compute the velocity distribution of the gesture, and apply rotation on the velocity domain.
virtual gesture
real gesture
Virtual gesture is nearly identical to real gesture.
Creating virtual gesture can enrich the prior knowledge.

## Slide 18: Our Solution -- OneFi
Overview:
A similarity-based one-shot learning framework
Alleviate Training Overhead
A self-attention-based backbone
A data augmentation method based on signal modeling
Base Dataset
Pre-processing
Data Augmentation
Support Set
Pre-processing
Extract Prior Knowledge
One-Shot Adaption

## Slide 19: Similarity-based one-shot learning framework
Support Set
Query Set
Feature
Extractor
Cosine Distance
…
…
…
Feature
Extractor
Classifier C1
Base Classes
Unseen Classes
Loss
Fix Weight
Stage 1
Train
Stage 2
Fine-tune
Encode Prior knowledge into the feature extractor
Finetune a new classifier C2 based on the support set
Lightweight one-shot learning framework
Alleviating the training overhead
Classifier C2
Query Feature
Cosine Distance

## Slide 20: Our Solution -- OneFi
Overview:
A similarity-based one-shot learning framework
A self-attention-based backbone
A data augmentation method based on signal modeling
Alleviate Training Overhead
Feature
Extractor

## Slide 21: WiFi Transformer: A backbone
Linear Projection of Time Patches
1
2
3
4
5
6
7
8
9
0
CLS
Transformer Encoder
Output
Position
Embedding
Transformer Encoder
Multi-Head Attention
Only needs O(1) sequential operations
Reduces the overhead of training the feature extractor
self-attention-based

## Slide 22: Evaluation Setup
Implementation
  Desktops with Intel 5300 NIC
Collect 40 difference gesture classes.
  20 as base dataset
    E.g. Draw ‘1’, Draw ‘2’, Draw ‘U’, Draw Circle, Draw Rectangle …
  20 as unseen dataset
    E.g. Draw ‘a’, Draw ‘b’, Slide, Sweep, Draw Zig-zag …

## Slide 23: Overall Accuracy
Upon six-unseen-gesture classification
Outperform MetaSense and RF-Net greatly

## Slide 24: Effect of Virtual Gestures
Virtual gesture generation is effective in enriching the prior knowledge and improving few-shot recognition accuracy.

## Slide 25: Training Overhead
OneFi entails significantly less training overhead.
WiFi Transformer help to relieve the training overhead.
Converge in 2 mins
Different learning frameworks
Different backbone networks

## Slide 26: Summary of other evaluation results
By adding more shots, OneFi can achieve high accuracy in 20-unseen-gesture classification.
OneFi works well with small number of WiFi receivers.
OneFi generalizes in cross-domain experiments.
(72% with 3 shots)
(1 or 2 receivers)

## Slide 27: Conclusion
We design OneFi, a one-shot WiFi HGR system. Extensive experiments demonstrate its strong ability to recognize unseen gestures.
We present a novel virtual gesture generation technique that significantly enriches the prior knowledge.
We propose a lightweight one-shot learning framework, together with a self-attention based backbone to alleviate training overhead.
Thanks! & Questions?